LEAP Tutorial

Training Addis Ababa,

April 2010

Peter Hoefsloot

1.	Examining images using the LEAP Viewer	2

2.	Determining Planting Dekads	10

3.	Understanding and calculating the Water Balance	17

4.	From Water Balance to yield reduction	28

# Examining images using the LEAP Viewer

The LEAP viewer is the central part of the software through which all input and output can be displayed in maps.

Checking for new data Manual: Paragraph 2.8 “Getting new data” Page 15 and 16.

Exercise  If you have an internet connection : check the server for new data.

Display data in the viewer Manual: Chapter 8 The LEAP image viewer Page 60 – 71

Exercise  Display the rainfall image (RFE2 dataset) for the third dekad of September 2005.

Exercise : For the boundaries select the zones.

Exercise  Zoom in to Addis Ababa. Addis contains about 4 complete pixels. Write down the values for these 4 pixels. Calculate the average rainfall for Addis by hand

| Pixel No. | Value |
| --- | --- |
| 1 |  |
| 2 |  |
| 3 |  |
| 4 |  |
| Average |  |

Exercise  Zoom out to Ethiopia and select the mask for the Meher areas

Exercise  Find the pixel with the highest rainfall within the Meher area. Note the following properties:

| Pixel | Value |
| --- | --- |
| Pixel Value |  |
| Latitude |  |
| Longitude |  |
| Pixel (row) |  |
| Line (column) |  |
| Name of the Region |  |
| Name of the Zone |  |
| Name of the Woreda |  |

Using LEAP output in bulletins (copying to MS Word) Manual: Paragraph 8.2.12

Exercise  Copy the image to the Windows Clipboard, Open Microsoft Word and paste the image into Word.

Exercise  Go Back to LEAP, move the cursor over the legend, press the right mouse button and use the function “Copy legend to Clipboard”. Paste the legend into Word below the image. Give the document a proper title.

Using data in Excel Manual: Paragraph 8.2.8

Exercise  Go Back to LEAP and use the function “Aggregate to Excel” to fill the table below.

| Zone “North Wollo” | Value |
| --- | --- |
| Number of pixels in the Zone |  |
| Approximate area in square kilometers the Zone covers, knowing that 1 pixel is approx. 100 km² |  |
| Average Rainfall in mm for the Second dekad of September 2005 |  |
| Same for first dekad of April 2005 |  |
| Same for third dekad of April 2006 |  |
| Same for third dekad of April 2004 |  |

Exercise  Display again the rainfall estimates (RFE2 dataset) for the third dekad of September 2005 and compare to normal rainfall

Exercise  Fill the following table. The first 2 rows are filled as an example.

| Zone | Qualification of Rainfall compared to average |
| --- | --- |
| South Wollo | More or less normal |
| South Gonder | Half of the Zone above average; Half of the Zone received normal rainfall |
| Jimma |  |
| East Harerge |  |
| Arsi |  |

Cumulative rainfall products

Exercise  Make a cumulative rainfall picture for 2010 (January 1 to April dekad 1).

Other parameters (example NDVI) Manual: Chapter 7

Exercise  Read about NDVI in Chapter 7 of the manual. Display NDVI for all the dekads in 2010 (from January dekad 1 to April dekad 1 by walking through the images in the viewer). Look specifically at the Belg and Rangeland areas

Exercise  Analyse the NDVI data for both the cropping areas (Belg) and the rangeland/pasture areas (Afar, Somali etc..).

| Area | Qualification of the season so far |
| --- | --- |
| Southern Belg Cropping areas |  |
| Northern Belg Cropping areas |  |
| Rangeland Areas |  |

Comparing different datasets for NDVI Manual: Chapter 7

NDVI is vegetation greenness. Dekadal composite images. In LEAP we have 2 satellites:

- NOAA at 800 km orbit, circles around the earth. Passes about 3-4 times per dekad. Advantage: archive dating back to 1981.

- Meteosat at 36.000 orbit, geostationary. Image every hour : 150 per dekad. Advantage: higher resolution and more images

Exercise . Display the NDVI image for the first dekad of March 2010 for the dataset USGS. Copy the NDVI data to Word. Then select the other NDVI dataset called “Meteosat”

and copy this dataset to Word as well. Both NDVI datasets should be side by side now with a legend.

Examine the images well and describe the similarities and the differences.

# Determining Planting Dekads

Preparations for planting dekad calculations Manual: Paragraph 4.4

Planting dekads are expressed in dekad numbers

|  | Dekad 1 | Dekad 2 | Dekad 3 |
| --- | --- | --- | --- |
| January | 1 | 2 | 3 |
| February | 4 | 5 | 6 |
| March | 7 | 8 | 9 |
| April | 10 | 11 | 12 |
| May | 13 | 14 | 15 |
| June | 16 | 17 | 18 |
| July | 19 | 20 | 21 |
| August | 22 | 23 | 24 |
| September | 25 | 26 | 27 |
| October | 28 | 29 | 30 |
| November | 31 | 32 | 33 |
| December | 34 | 35 | 36 |

Exercise   Suppose the crop is planted / sown at the second dekad of March. What is the number of that dekad?.

Exercise  Open the Belg Project.and make sure just one crop is selected: Maize_Belg

Exercise  For 2010 we have just RFE2 rainfall images available. So make sure RFE2 is in the data priority box under “actual rainfall data”.

Exercise  Open the zonal spreadsheet that underlies the Belg project: belg.xls, look-up the “Sowing Window Start Dekad” and the “Sowing Window Start Dekad” for Maize_Belg for zone Guji in Oromia.

| Item | Value |
| --- | --- |
| Sowing Window Start Dekad |  |
| Sowing Window End Dekad |  |

Exit the sheet (do not make changes)

Exercise 19. Planting dekads are calculated with actual rainfall data. Use the viewer to determine what the last available dekad is for RFE2 rainfall images in 2010..

| Item | Value |
| --- | --- |
| The last available dekad for RFE2 rainfall is |  |
| The first dekad where the planting calculation will look for planting opportunities |  |
| The last dekad where the planting calculation will look for planting opportunities |  |

Calculating planting dekads with a rainfall threshold Manual: Paragraph 4.4

Exercise  Now calculate the planting dekads for Maize Belg, 2010.

This is the planting rule we will assume: at least 20 mm of rainfall the first dekad and again 20 mm the dekad after.

Exercise  Display the image you just created in the LEAP viewer. In Guji, planting has been possible in some areas. The planting dekad is:

Exercise  Check the “Compare to normal” checkbox. Move your cursor over the image and determine where planting has been early and where planting has been late.

| Compared to a normal year, planting in 2010 has been early in the following zones. |  |
| --- | --- |
| Compared to a normal year planting in 2010 has been late in the following zones. |  |

Exercise  Let’s verify the planting dekad calculation. Display the RFE2 rainfall image of the First dekad of April 2010 in the viewer. Move the cursor to Guji (see above). Press the right mouse button and select “View trend”. You will see the average rainfall for Guji (all pixels). Now calculate the planting dekad for Guji by hand.

Exercise  Now re-calculate the planting dekad with another rule: 10 mm the first dekad and 0 mm the second dekad. Answer the following questions

| The calculated planting dekads will be lower (earlier in the year). Why? |  |
| --- | --- |
| The planting dekad for Bale Zone is now: |  |

Exercise  We will now generate a picture that displays areas where planting occurred on or before dekad 8 and after dekad 6. Recalculate the planting dekad with the normal 20+20 rule again. Then display the planting dekad image again. Then move your cursor to the legend and press the right mouse button, then press “Edit Legend”

Change the legend on the left side, to the one on the right

Press Ok. You see:

Exercise  Edit the legend again and now save the legend for later use with the name “Planting Workshop.clr”

# Understanding and calculating the Water Balance

Understanding the Water Balance Manual: Paragraph 4.4

The objective of the water balance model is to convert raw observations of the atmospheric environment into a set of parameters which are of direct importance for crop production. Those parameters include:

- the "Actual Evapotranspiration" (ETA), which is the amount of water actually used by the crop excluding runoff;

- the amount of excess of water which may damage crops through water logging;

- a Water Satisfaction Index (WSI) which expresses which percentage of the crop's water requirements were actually met.

Basically, the water balance is the difference between the effective amounts of rainfall received by the crop and the amounts of water lost by the crop and the soil due to the evaporation, transpiration and to deep infiltration. The amounts of water, held by the soil and available to the crop, is also taken into account. In practice, the water balance is computed using a book-keeping approach.

Actual and reference evapotranspiration

Through experimentation Penman found that that it was possible to calculate a “crop neutral” reference evapotranspiration (ET0) based on 4 basic meteorological parameters:

- Wind

- Solar radiation

- Temperature

- Humidity

Many meteorological stations around the world measure these parameters making it possible to calculate ET0. Some of these input 4 parameters can be estimated from others.

Reference evapotranspiration (ETo or sometimes referred to as potential evapotranspiration) is defined as the evapotranspiration from a 10cm tall grass that completely covers the ground, and is supplied with adequate water. Many scientists refined Penman’s work. FAO / United Nations has standardized on the adaptations by Montheith.

Crop coefficients

The relation between actual and reference evapotranspiration and actual evaporation in the field is based on crop coefficients. ETa is determined by the crop coefficient approach whereby the effect of the various weather conditions are incorporated into ET0 and the crop characteristics into the Kc coefficient:

ETa = Kc * ET0

The effect of both crop transpiration and soil evaporation are integrated into a single crop coefficient. In other words, the Kc coefficient incorporates crop characteristics and averaged effects of evaporation from the soil. Crop coefficients (Kc) are dependent on:

- Crop

- Phenological stage of the crop (planting, vegetative phase, yield formation, ripening etc..)

- Soils, climate etc. Crop coefficients are known to be slightly different for different parts of the world.

Exercise  Read Chapter 4.1 Page 39. Examine the Crop coefficients for Teff

Calculating the Actual Water Balance

The water Balance is forward looking! Predict WRSI to the end of the season using normal rainfall.

The computation is done dekad-by-dekad (DEK) and it starts before the planting to take into account previous rainfall amounts stored into the soil. From the planting dekad, the crop water requirements (WR) are calculated as the potential evapotranspiration (PET) times the crop coefficient (KCR) values.

WR = ET * KCR   (1)

IF actual rainfall data (ACT) are available these are used, otherwise the calculation uses normal rainfall data (NOR). The rainfall used in the calculations is called the working rainfall (WRK). So for a dekad the following is valid:

If ACT is missing 	then WRK = NOR

If ACT is not missing  then WRK = ACT

The available water amount (AvW) is the difference between the crop water requirements and the working rainfall (WRK).

AvW = WRK - WR

Surplus or deficit (S/D) result from the water budget between the soil water storage (SW), ranging between the field capacity and the permanent wilting point, depending on the root depth, as well, and the soil water holding capacity (WHC).

SW = SW of previous dekad + AvW.

And

0 < SW < WHC

In the final column, the water requirements satisfaction index (INDEX) summarizes, up to a specific growth stage or the end of its development, the degree to which cumulative crop water requirements have been met. The WRSI represents, at any time of the growing period, the ratio between the actual and the potential evapotranspiration.

If SW (previous dekad) + WRK > WR then INDEX remains the same

If SW (previous dekad) + WRK < WR then INDEX drops proportionally

Exercise  Fill the yellow holes in the following water balance calculations:

Calculating the water balance Manual: Paragraph 5.1

Exercise  Calculate the Water Balance for 1 crop, for just 1 season

Exercise  LEAP will give you status messages. Describe clearly what these messages mean

| One or more actual rainfall files not found (using normal rainfall)... |  |
| --- | --- |
| Using normal ET0 (actual ET0 not available)... |  |
| Total number of Water Balance Calculations (pixels): 18445 |  |
| Calculation succeeded: 4034 |  |
| Missing Planting Dekad: 1769 |  |

Exercise  The final index of a Water Balance calculation is called the WRSI. Display the WRSI in the viewer.

Exercise  Move your cursor to the northern areas (a colored pixel) and with the right mouse button view Water Balance details.

Exercise  Please answer the following questions:

| Why do you find -999 in the ACT column |  |
| --- | --- |
| The final WRSI value for this pixel is |  |
| What does this WRSI value mean in terms of crop yield forecasting (see image legend) |  |
| In which crop phase, the highest water deficit is expected? |  |

Exercise  In the LEAP viewer compare the WRSI to Normal. Please give an indication of the expected WRSI compared to normal in the North, South and Eastern areas

| North and South Wollo |  |
| --- | --- |
| South (Gamo Gofa) |  |
| East (Jijiga) |  |

Exercise  Now display the Total Water Deficit. Find the pixel with the highest deficit in millimeters of moisture

| The pixel with the highest water deficit is located in zone: |  |
| --- | --- |
| The WRSI for that pixel is: |  |

Exercise  Please check whether there are areas with water excess.

| In which zones water excess is taking place (or is expected) |  |
| --- | --- |
| In which growing phase of the crop does water excess occur? |  |
| Is the crop during this phase vulnerable for water excess? |  |

Exercise  Now calculate the Water Balance for the years 2006-2010 (5 years)

Exercise  Export all the WRSI values for these years to Excel

Please note that the number of pixels on which these exported data are based can differ from year to year.

Exercise  Why do you see 1 or 2 empty cells for certain zones?

Exercise  In Excel, make this chart for Bale

WRSI can be calculated for Rangeland as well:

- Continuous calculation (36 dekads in a year)

- Based on 5 dekad cycle length (arbitrary)

- Based on a cop coefficient of 1.

Exercise  Look at WRSI for Rangeland for 2010

Exercise  Give an estimation of the development of grazing conditions in 2010 in the following areas:

| Afar |  |
| --- | --- |
| Somali |  |
| Southern Oromia |  |

# From Water Balance to yield reduction

Relation between crop water use and yield

Doorenbos and Kassam outlined in their FAO publication “Yield response to water” that there is a clear relation between crop yield and water use. This relation is the basis of the use of a water balance calculation in crop forecasting. It is possible to establish a maximum yield (Ym) based on a season without water stress and water deficit. The total evapotranspiration is then at his maximum (ETm). In semi-arid circumstances yield is usually reduced due to water stress leading to a lower actual yield (Ya) and lower actual evapotranspiration (ETa)

Yield Reduction is the percentage reduction compared to a yield obtained without water stress.

It is therefore not measured against maximum yield!

Yield response to water

The authors introduced the so-called yield response factor (ky) to explain the yield reduction due to water stress. They established the yield response factor for a large number of crops in a limited number of climates. Doorenbos and Kassam found this relation to be near-linear for most crops (see graph). The general formula is:

(1- Ya/Ym) = ky * (1 - ETa/ETm)

The graph below establishes the relationship for a number of crops.

Horizontal axis: Yield from 0 (no water stress; high yield) to 1 (100% water deficit; no yield)

Vertical axis: Evapotranspiration deficit from 0 (no deficit) to 100 (100% deficit)

In LEAP the Yield Reduction can be calculated from Total Actual Evapotranspiration (ETa) and Total Water Requirement (TWR, same value as ETm), with the formula:

100-((1-(1-ETa/TWR)*Ky)*100)

Ky is a crop specific value stored in LEAP

Exercise  Calculate the Yield Reduction

| The Ky for Maize is: |  |
| --- | --- |
| Assume the Total Water Requirement for maize in a given season is 401 mm. The Actual Evapotranspiration in that season is 343 mm. What is the yield reduction percentage? |  |

Exercise  Now calculate the predicted Yield Reduction in LEAP for Maize (Belg season) for 2010.

Exercise  Now display the yield reduction in the viewer. Change the legend to the legend below:

Answers to Water Balance Exercise